## Slide 1
Carbon DT
A building-energy screening MVP that converts raw utility bills into expected usage, diagnostics, operational recommendations, and carbon/compliance outputs.
Uploaded bills + Open-Meteo
Problem Being Solved
Utility-bill data is hard to compare month to month without normalization
Owners need a fast first-pass answer before a full engineering audit
Results must be explainable enough for operators, not a black-box model
Core Output
Monthly electricity and gas records normalized to kWh and therms
Expected-vs-actual energy baseline adjusted for weather and season
Diagnostics, deterministic recommendations, emissions, and LL97 screening
Current Delivery Mode
Public Streamlit web app with CSV upload
Historical weather fetched from Open-Meteo by ZIP or address
No embedded customer files, secrets, or LLM dependency

## Slide 2
How The Solution Works
Concrete data flow from uploaded bills to expected usage and recommended actions
1. Utility Bill Ingestion
CSV input requires: billing_start, billing_end, utility_type, usage, usage_unit, cost
Electricity is normalized to kWh and gas to therms
Billing periods spanning multiple months are prorated into monthly records
2. Weather And Monthly Features
Open-Meteo returns historical daily mean temperature for the billing window
The app aggregates to monthly avg_temp and calculates HDD/CDD at a 65F base
It also creates month index, season flags, and energy-per-sqft features
3. Expected Energy Calculation
Electricity and gas are modeled separately because their drivers differ
If history is sufficient, a simple sklearn linear regression is fit for explainability
If history is sparse, the app falls back to a weather-normalized heuristic baseline
4. Diagnostics To Action
Rules detect patterns such as high electricity, winter gas spike, baseload, and negative trend
Recommendations come from a fixed library mapped to each diagnostic
Ranking uses a transparent weighted formula based on severity, confidence, category, and difficulty
Example baseline logic: predicted electricity intensity uses month index, CDD, HDD, summer/winter flags; gas uses HDD, CDD, heating season, and winter flags. Output is predicted intensity x floor area.

## Slide 3
Current MVP Status And Next Steps
Where the product is credible today and what should improve before larger rollout
What Is Already Working
Upload-driven screening workflow with validation messages
Weather-aware expected usage for electricity and gas
Deterministic diagnostics and recommendation ranking
Annual emissions calculation and NYC LL97 penalty estimate
Downloadable PDF report for audit-style output
Important Assumptions
This is a single-building MVP, not a portfolio platform yet
Weather quality depends on correct ZIP/address geocoding
Savings and carbon ranges are heuristic placeholders
Expected usage is for screening and triage, not investment-grade M&V
Recommended Next Moves
Deploy and validate with real customer bills
Measure cold-start and weather-fetch latency with production telemetry
Calibrate diagnostics and recommendation heuristics with audit outcomes
Then add API separation, stronger UI, and portfolio support
Positioning: strong for fast building-level audit screening and operator guidance; not yet a substitute for full engineering analysis or enterprise workflow software.